## Slide 1: CS4101 Introduction to Embedded Systems Lab 8: Arduino DAC and PWM
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Lab 8
Basic 1: based on Basic 1 of Lab 7 (30%)
  Repeat Basic 3 of Lab 7, but with two buttons to two LEDs.
  Handle all events by interrupts instead of polling.
Basic 2: PWM (20%)
  Replace one of the two LEDs in Basic 1 by a RGB LED
    When the corresponding button is down, RGB LED turns red.
    When the button is released, flash the RGB LED in yellow (R=255, G=255, B=0) at 1Hz (on 0.5 sec and off 0.5 sec) for the same amount of time as the pressed time.
    Note: The RGB LED must be connected to a PWM pin.

## Slide 3: Lab 8
Basic 3: step motor (20%)
  Replace the other LED in Basic 2 by a step motor.
    When the corresponding button is down, turn the step motor clockwise continuously.
    When the button is released, turn the step motor counterclockwise continuously for the same amount of time as the pressed time.
Basic 4: joystick (30%)
  Replace the button to the RGB LED with a joystick and use the button on the joystick as the button.
  When the button is down, RGB LED shows colors based on the position of joystick: (R=xAxis/4, G=yAxis/4).