## Slide 1: CS4101 Introduction to Embedded Systems Lab 11: Task Communication
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Lab 11
Basic 1: Moving Control (40%)
  Connect LCD and Keypad to your Arduino UNO.
  Use the Keypad to move a dinosaur on LCD.
    Use button “2” for up, ”8” for down, “4” for left, “6” for right.
    Initialize dinosaur on position (0,0).
    You should avoid the dinosaur from running out of the edge.
  Create two tasks, “controlTask” and “displayTask”.
    controlTask: Read inputs from Keypad, calculate position of the dinosaur, inform displayTask of the position through a queue. No LCD-printing, but serial printing is allowed.
    displayTask: Receive position information from the queue and display the dinosaur. No calculation in this task.

## Slide 3: Lab 11
Basic 1: (cont.)
  Constraints:
    Only variables used by the I/O modules could be declared as global. Any other global variables are not allowed.
    Use only queue to communicate between the two tasks.
    Only one queue is allowed.
  The dinosaur:
    Use the “byte err_dragon[8]” in page 5.

## Slide 4: Lab 11
Basic 2: Cactus Strikes Back (60%)
  Extend Basic 1.
  Start of the game:
    Dinosaur and Cactus are initialized randomly on the field of size 2*16.
    The dinosaur has 3 eggs to lay.
  Game rules: lay all eggs where they will not be broken
    Move the dinosaur as in Basic 1.
    When the dinosaur reaches a cell, she can just pass by or lay an egg there by pressing button “5”.
    Each time when the dinosaur makes a move, the cactus moves as well, to any possible direction it can reach from the current cell.

## Slide 5: Lab 11
Basic 2: (cont.)
  Game rules: (cont.)
    Note that cactus must make a move when the dinosaur moves, i.e., it cannot stay on its current position.
    The game ends when
      Cactus steps on one of the egg. Display the “broken” (see page 5) character for 1 sec, followed by “Game over” for 1 sec. Then, restart the game.
      Dinosaur successfully lays the third egg and all eggs are well-preserved. Display “Succeed!” for 1 sec and restart the game.
  Implementation:
    Can use more than one queue. But beware of the number and the size of your queues.
    See: https://drive.google.com/drive/folders/1-AYftlE3WCcn3IZZzNVF0BWpvbc1SPk2?usp=sharing

## Slide 6: Lab 11
byte err_dragon[8] = {B00111, B00101, B00110, B00111, B10100, B10111, B01110, B01010}; byte cact[8] = {0x04, 0x05, 0x15, 0x15, 0x16, 0x0C, 0x04, 0x04}; byte egg[8] = {0b00000, 0b01010, 0b11111, 0b11111, 0b11111, 0b01110, 0b00100, 0b00000}; byte broken[8] = {B00100, B10101, B01110, B11111, B11111, B01110, B10101, B00100};